	Function	Provenance	The fine print
0	Exit
1	Random-Raster	New Python code	Reinforcement for the idea that a Vector display is sensitive to refresh rate, but is not a Raster display!
2	Tic-Tac-Toe For Two Game	New Python code	Illustrates use of multiple displays. Requires two analog scopes
3	Tic-Tac-Toe against WW	New WW code	Interactive game played with Light Gun and CRT display
4	R-196 Bounce	WW Report R-196	~30 lines of code from Whirlwind Programmer Training Manual R-196, with a couple of mistakes fixed.
5	Bounce with Hole	WW R-196 example	Complete Bounce program with Hole-in-the-Floor and automatic trajectory adjustment. Precursor to a ‘game’ version.
6	Mad Game	WW tape	Good example of simple Light-Gun/CRT input/output. No known application.
7	Blackjack Game	WW tape	Play Blackjack against Whirlwind with Light Gun and CRT. No documents found; probably an unauthorized hack
10	CRT Test Pattern	WW tape	Simple pattern generator to check analog gain settings in the CRT drivers
11	Vibrating String fixed ends	WW tape	DCL-090 “Vibrations in a Length of String” / LMIR - No. of points (p); default = 0.00400 / RMIR - Magnitude of string displacement (m); default = 0.40000 / FF #2 - Scope amplitude adjustment; default = 0.00010 / FF #3 - Elasticity factor; default = 0.70000
12	Vibrating String open end	WW tape
13	Nim	WW tape	DCL-113 / “Removing pieces from the groups is done by setting the / desired number in Right MIR and the address in Left MIR using the rightmost column where the groups are 0-7 for A-H consecutively. Pressing Upper Activate button will read in the above amount and display the new numbers in the groups. 'm' removals have to be made in each move; if less than m are desired, 0 has to be removed until m removals are completed. After m removals have been done, Upper Activate button has to be pressed for computer move.”
14	Number Display	WW tape	Displays incrementing number pattern in Binary, Decimal, Octal, Hex (“Sexadecimal”) with dot-matrix character generator
15	Air Defense	WW M-1343 code	SW-D: Down=Target, Up=Interceptor
16	Vector Clock	New WW code	Click the center point to toggle between minimal and a more detailed (and flickery) rendering
17	Lorenz Attractor	New WW Code	New code, but using the actual Whirlwind floating point library. (Lorenz Attractor was discovered in 1963, after WW at MIT. This code thanks to Angelo Papenhoff!)

Whirlwind Demo Menu Secret Decoder Chart; Apr 11, 2025

See https://github.com/gfedorkow/Whirlwind-Instruction-Simulator
for code samples